## Slide 1: Self-Supervised Transformer Imputation for Reliable Prognostics Under Missing Data
Austin Coursey and Abel Diaz-Gonzalez

## Slide 2: Problem Motivation
Being able to determine the remaining useful life (RUL) of a system or component is important
  Safety, maintenance, reliability
Many data-driven solutions to RUL estimation assume no missing data
  Is this realistic? What if something goes wrong?
We need to be robust to missing data
Airplane engine failure. Credit: https://nymag.com/intelligencer/2021/02/watch-terrifying-video-of-united-328-in-flight-engine-fire.html

## Slide 3: Existing Solutions
Classic approaches
  Linear interpolation, SVMs, backfill, etc.
Recent approaches
  Largely GANs [1,2,3], Gaussian Process Regression [4]
Most do not consider temporality
  Multivariate time series data
What about transformers?
  Have been used for time series imputation [5]
  Reconstructing masks has also been used for self-supervised learning [6,7,8]

## Slide 4: Method
Sensor data with deleted values
Reconstructed sensor data
E
R
Encoder Block
Recons. Head
z
X’
Transformer
E
RUL
Encoder Block
RUL Head
RUL Prediction
Reconstructed sensor data
Pretext Task (Pretraining Loop)
Transformer can impute missing data [5]
Learning to impute missing data may lead to useful representations for RUL predictions
Rationale
…

## Slide 5: Results
Trained models 10 times on aircraft engine failure (simulated) dataset
Finding:
  SSL only slightly helped
  Transformer imputation only slightly better than linear interpolation
Why?
  Dataset small (80 train flights, 20 test, ~20,000 train samples)
  Masking algorithm too easy
    Linear interpolation may be good enough here
Model | Mean RMSE(SD)
No SSL’ | 13.71(2.32)
Only Latent*’ | 56.34(1.43)
Latent + Input*’ | 12.99(0.76)
Linear Interpolation | 14.00(1.39)
*uses SSL
‘uses Transformer Imputation

## Slide 6: Sources
[1] Hyunsoo Lee, Seok-Youn Han, and Kee-Jun Park. Generative adversarial network-based missing data handling and remaining useful life estimation for smart train control and monitoring systems. Journal of Advanced Transportation, 2020:1–15, Nov 2020
[2] Chen Wenbai, Liu Chang, Chen Weizhao, Liu Huixiang, Chen Qili, and Wu Peiliang. A prediction method for the rul of equipment for missing data. Complexity, 2021:1–10, Dec 2021.
[3] Yu Huang, Yufei Tang, James VanZwieten, and Jianxun Liu. Reliable machine prognostic health management in the presence of missing data. Concurrency and Computation: Practice and Experience, 34(12), May 2020.
[4] Pham Luu Trung Duong and Nagarajan Raghavan. Prognostic health management for led with missing data: Multi-task gaussian process regression approach. In 2018 Prognostics and System Health Management Conference (PHM-Chongqing), page 1182–1187, Chongqing, 2018. IEEE.
[5] A. Yarkın Yıldız, Emirhan Koc, and Aykut Koc. Multivariate time series imputation with transformers. IEEE Signal Processing Letters, 29:2517–2521, 2022.
[6] Yiwei Fu and Feng Xue. Mad: Self-supervised masked anomaly detection task for multivariate time series. In 2022 International Joint Conference on Neural Networks (IJCNN), page 1–8, Padua, Italy, Jul 2022. IEEE.
[7] Wenrui Zhang, Ling Yang, Shijia Geng, and Shenda Hong. Cross reconstruction transformer for self-supervised time series representation learning. May 2022. arXiv:2205.09928 [cs].
[8] Zhe Li, Zhongwen Rao, Lujia Pan, Pengyun Wang, and Zenglin Xu. Ti-mae: Self-supervised masked time series autoencoders. Jan 2023. arXiv:2301.08871 [cs].